## Slide 1: PLYWOOD
Plywood is a panel product consisting of thin wood veneers (plies) glued together so that the grain direction of each layer of veneer is perpendicular to that of the adjacent layers.
An uneven number of veneers is required to form balance in the sheet and keep the sheets flat and stable.
INTRODUCTION

## Slide 3: Sliced veneers
Sliced veneers, as depicted in the upper portion of the above figure, are used for furniture, cabinets, paneling, and other decorative and architectural purposes. The logs are sawn to produce flitches with the correct grain orientation and the flitches are sliced.

## Slide 5: Veneer quality
Grade A | Grade S | Grade B | Grade C | Grade D | Grade PG
Description: | Description: | Description: | Description: | Description: | Description:
A high quality appearance grade veneer suitable for clear finishing. | An appearance grade veneer which permits natural characteristics such as knots as a decorative feature subject to agreement. | An appearance grade suitable for high quality paint finishing. | A non-appearance grade with a solid surface. All imperfections such as knot holes or splits are filled. | A non-appearance grade with permitted open imperfections. Limited number of knots and knot holes up to 75mm wide are permitted. | A non-appearance grade that has open imperfections such as holes, knots, splits and rough grain.
Applications | Applications | Applications | Applications | Applications | Applications
Textured exterior cladding Interior wall lining Interior ceiling lining Furniture & joinery | Decorative applications Interior wall lining Interior ceiling lining | Furniture & joinery Concrete formwork Primary sheathing Signs Engineered components | Concrete formwork Gussets Roof decking Flooring Sub sheathing Bins, boxes & crates Stressed skin panels Hoardings | Structural components Beams & portals Roofing Bracing Utility buildings | Temporary security covers Pallets Fillets & liners General packaging Crates
Plywood is classified according to grades, which are based on face and back veneer quality. The Plywood Association of Australia (PAA) grading standards are as specified in the following table.

## Slide 6: Term plywood
Traditional plywood construction
with odd number of veneer plies in alternate directions with neutral axis being in the plane of the middle of the centre veneer. May be any number of odd plies depending predominantly on thickness.
5-ply blockboard
consisting of central core of sawn timber battens sandwiched between two veneers each side of the panel
Laminboard
consisting of a central core of slats or
veneers at right angles to
the two veneers each side of the panel, producing a long grain appearance.

## Slide 7: Standard sizes (mm)
Plywood is available in several lengths and widths and a wide range of thicknesses. Non-standard panel sizes are available on request from manufacturers.
However, the most common plywood panel dimensions (mm) are 2400 X1200 and
2700 X1200mm.
Sheet sizes (mm) for plywoods include:
2400 X1200 2400 X 900
2100 X 1200 2100 X 900
1800 X 1200 1800X 900
2700 X 1200
A 2250 mm length panel is often specified for flooring applications, as this size suits the standard floor joist spacing of 450mm. Flooring plywood is usually supplied with a plastic tongue and grooved long edges.
Plywood wall bracing is available in 2440 mm and 2745 mm lengths to preserve 2400 and 2700 floor to ceiling height after installation of ceiling and flooring.

## Slide 8
Plywood thickness will vary with manufacturer and product application. Standard panel thicknesses
range from 3 mm up to 25 mm.
Structural – 3, 4, 4.5, 6, 7 12, 13, 15, 17, 19, 21, 25 mm
Marine, exterior and interior – 3, 4, 6, 9, 12, 16, 19, 25 mm
Thicker panels are available from some manufacturers for special applications e.g. 150 mm thick
plywood used as bridge decking. Larger panel sizes can be produced by scarf-jointing.
Standard thickness: (mm)
Application | Thicknesses | Stress Grade
Lining panels | 3 – 15 | N/A
Residential flooring | 13, 15, 17 | F11, F14
Industrial flooring | 17 – 25+ | F11 – F22
Diaphragms | 9 – 15 | F11, F14
Bracing (shearwalls) | 3 – 15 | F11, F14, F27
Box beams | 7 – 12 | F11, F14
Portal frame gussets | 12 - 25 | F11, F14
Stress Grades
The characteristic strength and stiffness values of structural plywood are allocated via the F- grade
classification system and are given in AS 1720.1 SAA Timber Structures Code, Section 5 and
AS/NZS 2269, Plywood – Structural. Refer to section on engineering design

## Slide 9: Bond Quality
Four types of glue bonds are defined and specified in AS 2754.1 Adhesives for plywood Manufacture. The bond types are A, B, C and D, in decreasing order of durability under conditions of full weather exposed.
A Bond | Phenol, Resorcinol or Tannin Formaldehyde | Fully weather resistant
B Bond | Melamine fortified Urea Formaldehyde | Partially weather resistant (2-5 years exposed)
C Bond | Urea Formaldehyde | Interior glue - high humidity applications
D Bond | Extended Urea formaldehyde | Interior glue - low humidity applications

## Slide 10: type OF PLYWOOD
Renewable Resource - A natural product from a renewable resource. Beautiful - Preferred because of its warmth and natural markings. Strength - Unique cross-layered structure makes it kilo for kilo, stronger than steel. Efficiency - Uses more of the log than timber. Versatility - Can be bent and formed to meet various sizes and shapes. Durability - Long-lasting and good resistance to damage.
Plywood can be broadly classed as either ‘Exterior’ plywood or ‘Interior’ plywood. Veneer quality, glue type and timber species are the major contributing factors that determine the application of a plywood panel.
BENEFITS OF PLYWOOD

## Slide 11: Plywood product
Structural Plywood
Structural Plywood is manufactured to AS/NZS 2269 from softwood veneers. It is available in grades based on face and back veneer quality from A to D,
with a minimum F8 stress grade.
Structural Plywood is a very stable and workable
type of plywood, with numerous applications for the
building, shopfitting and cabinet making industries.
The most common grades of structural plywood available are CD and DD.

## Slide 12: Plywood product
Exterior Plywood
Local Exterior Plywood is manufactured to AS/NZS 2271 and intended for use in
non-structural, exterior applications
where a high quality aesthetic finish is required.
Imported exterior plywood may be
manufactured to other international
standards other than PAA, such as IHPA*or the JPIC grading standards.
description

## Slide 13: Plywood product
description
Exterior Plywood

## Slide 14: Plywood product
Formwork Plywood
Formply is made of a high-density overlay (HDO) of phenolic resin impregnated
paper bonded to plywood.
Formply is idea for concrete formwork.
The overlay helps to protect the hardwood face veneer as well providing a sound
surface for the poured concrete.
It is manufactured to Australian Standards AS/NZS 2269.
description

## Slide 15: Plywood product
Marine Plywood
Marine plywood is a premium quality plywood made of selected wood
species based on density, bending
strength, impact resistance and
surface finish characteristics.
Manufactured with an A-grade
sanded surface face on both sides, as per the AS/NZS 2272 standard, with no core gaps and a permanent waterproof A-bond glue.
description

## Slide 16: Plywood product
Plywood Flooring
Tongue and Groove Plywood is strong and durable,
with a pre-sanded C-grade face panel available in
arange of thicknesses suitable for use in structural
and non-structural flooring. It has a machined
groove along its edges, with a single plastic tongue
to form a tongue and groove joint between sheets.
description

## Slide 17: Plywood product
Paper and Polyester Overlay Plywood
We offer a comprehensive range of polyester and paper overlay plywood’s available for use in interior applications such as wall and ceiling panelling. Gunnersen stock a variety of paper and polyester plywood. On request all paper designs can be coated with either the Rezilience finish to improve wearability and stain resistance, or the durable gloss/matt finish of polyester. Minimum quantities and lead times apply. Please contact your local Gunnersen branch for further information.
description

## Slide 18: Plywood product
Interior Plywood
Interior plywood is intended for use in non-structural, interior applications where a high quality aesthetic finish is required. Our range of interior plywood includes a variety of hardwood species such as Meranti, Melapi, Nyatoh, Sliced Pacific Maple, Hoop Pine and Radiata Pine amongst others sourced from plantations and sustainable forests, locally and overseas.
description

## Slide 19: Plywood product
Non structural Plywood
Speciality plywood available for the forming of curved surfaces in applications such as wall panelling and ceiling lining
description

## Slide 20: Plywood product
Shadowclad
Shadowclad® is a full exterior structural plywood that can be used for both decorative and bracing purposes available either primed or unprimed.
PLYWOOD CLADDING FOR BRACINGS & DECORATIVE EXTERIORS
Shadowclad inspires the designs of many leading Australian architects. Being a cladding and bracing material in one means that it is particularly cost-effective too.
With proven strength and durability, Shadowclad materials withstand the elements, offering architects, designers, builders and renovators a range of reliable design options. Their textured finish and weathergrooves are designed especially for exterior use.

## Slide 21
What are the requirements of marine plywood?
1. Water Proof adhesive
2. ALL Veneers are B grade or better.
Softwood plywood grades are the combination of the face veneer and the back veneer.
Examples are: A-C Face is A grade and Back is C grade C-D Face is C grade and Back is D grade B-B both Face and Back are B grade.
What are the requirements of exterior plywood?
1. Exterior (water proof) adhesive.
2. ALL Veneers (face, back or in the middle) are C grade or better.

## Slide 22: Handling
Panels should be unloaded so that no damage to pallets or bundles will occur. Metal
slings, hooks or chains should not be in contact with the panels. The panels should be removed from pallets or bundles by hand, taking care not to damage edges or faces by
dropping them or dragging them along the ground. When lifting panels by fork-lift truck
care must be taken to prevent the panels being damaged.
http://www.arcspace.com/books/Bent_Ply/bent_ply_book.html

## Slide 23: Storage
Panels should be stored horizontally under cover in their
original packing in conditions of moisture and temperature
similar to those in which they are to be used.
Increased moisture content and temperature variation may
cause internal stresses, thickness swelling or surface defects.
Stack panels on a firm raised base, with enough bearers to
prevent sagging.
Cover the stack to protect the top and the edges from
moisture penetration.
During prolonged storage it is recommended to relieve the
original strapping to prevent leaving a mark on the top and
bottom panels in the stack.
If film-faced formwork panels need to be stored temporarily
outdoors cover them with tarpaulins.
Care must be taken to prevent the panel edges being subjected to rain, splashing or ground water.